## Slide 1: UCIe SBINIT & MBINIT
V.SRAVANTHI
CHIPWEAVE TECHNOLOGIES PVT LTD

## Slide 2: CONTENTS
INTRODUCTION
SBINIT
MBINIT
MBINIT.PARAM
MBINIT.CAL
MBINIT.REPAIRCLK

## Slide 3: Introduction
UCIe (Universal Chiplet Interconnect Express) is an open, layered, multi-protocol capable, on-package interconnect standard for connecting multiple dies on the same package.

## Slide 4: UCIe Layers
How data is formatted (Protocol Layer)
How data is managed reliably (D2D Adapter)
How bits are physically transferred (Physical Layer)
Plus, packaging, compliance, and debug rules

## Slide 5
Link Training State Machine

## Slide 6: SBINIT
The sideband (SB) interface is initialized and repaired (when applicable).
When not performing the actions relevant to this state:
• UCIe Module main band (MB) Transmitters remain tri-stated
• MB Receivers are permitted to be disabled
• SB Transmitters continue to be held Low
• SB Receivers continue to be enabled
The SB initialization procedure is performed at 800 MT/s with 800 MHz sideband clock.

## Slide 7: SBINIT(Advanced Package)
Advanced Package has redundant SB clock and SB data Lanes (DATASBRD, CKSBRD) in addition to DATASB and CKSB.
Die0 TX sends a simple pattern in sync with clock
    TX sends 64 UI (Unit Interval) of 101010… pattern + 32 UI Low.
    On DATASB and DATASBRD in synchronous with CKSB and CKSBRD respectively.
Die1 RX samples the incoming message pattern w.r.t to both incoming clocks CKSB and CKSBRD.
3.Out of 4 data clock combinations, 1 pair is chosen who detects 2 times 64 UI patterns. ie. 128 UI pattern
Data | Clock
DATASB | CKSB
DATASB | CKSBRD
DATASBRD | CKSB
DATASBRD | CKSBRD

## Slide 8: SBINIT Advanced Package(Contd..)
  4.If at least one combo works,
    Die1 Receiver tells transmitter send 4 more pattern burst then stop.
    Die0 Transmitter:
      Sends 4 more pattern bursts + 32 UI low
      Then stops
      This extra delay ensures both sides are fully out of reset then both Dies can communicate through sidebands.
  5.If no data-clock combinations works based on pattern detection, Die0 TX sends
    (1 ms duration pattern + 1 ms zeros) for 8 ms duration.
    After 8 ms, timeout error happens “TRAINERROR”

## Slide 9: SBINIT Advanced Package(Contd..)
6.If multiple data-clock combinations works choose one based on priority as follows:
    DATASB / CKSB
    DATASB / CKSBRD
    DATASBRD / CKSB
    DATASBRD / CKSBRD
7 to 10 :
Module sends continuous sideband message on both TXDATASB and TXDATASBRD w.r.t TXCKSB and TXCKSBRD for 8 ms, if no response from partner timeout occurs TRAINERROR
Both Die 0 and Die1 must apply Sideband Data/Clock assignment (called the functional sideband) based on the information included in the {SBINIT Out of Reset} sideband message

## Slide 10: SBINIT(Standard Package)
1.Die0 TX sends a simple clock pattern​
TX sends 64 UI (Unit Interval) of 101010… pattern -> 32 UI LOW + 32 UI High.​
On DATASB in synchronous with CKSB respectively.​
2.Die1 RX samples the incoming message pattern w.r.t to both incoming clocks CKSB.​
​
Data ​ | Clock​
DATASB​ | CKSB​

## Slide 11: SBINIT Standard Package(Contd..)
3.Detection is successful when 2 times 64 UI patterns are detected. ie. 128 pattern by Die1 Rx.​
4.​If detection is successful Die1 RX tells Die0 TX send 4 more pattern burst then stop.​
Die1 Transmitter:​
Sends 4 more pattern bursts​
Then stops​
This extra delay ensures both sides are fully out of reset then both Die can communicate through sidebands.​

## Slide 12: SBINIT Standard Package(Contd..)
5.If pattern is not detected by Die1 Rx, Die0 TX sends​
(1 ms duration pattern + 1 ms zeros) for 8 ms duration.​
​ After 8 ms, timeout error happens “TRAINERROR”.
6 to 8 :​
​
Module sends continuous sideband message on both TXDATASB w.r.t for 8 ms, if no response from partner timeout occurs TRAINERROR

## Slide 13: MBINIT
In this state, the mainband (MB) interface is initialized and repaired or width degraded (when applicable).
The data rate on the mainband is set to the lowest supported data rate (4 GT/s).
For Advanced Package interconnect repair may be needed. Sub-states in MBINIT allows detection and repair of data, clock, track and valid Lanes.
For Standard Package, where no Lane repair is needed, sub-states are used to check functionality at lowest data rate and width degrade if needed

## Slide 14
Main band Initialization and Repair Flow

## Slide 15
This state is used to perform exchange of parameters that are required to set up the maximum negotiated speed and other PHY settings.
The following parameters are exchanged over sideband with UCIe Module Partner:
1.Voltage swing: The five bit value indicates the Transmitter voltage swing to the UCIe Module Partner.
The UCIe Module Partner must use this value and its Receiver termination information to set the reference voltage (Vref) for its Receivers.
The corresponding bits in {MBINIT.PARAM configuration resp} are reserved.
MBINIT.PARAM

## Slide 16
MBINIT.PARAM(Contd..)

## Slide 17
2.Maximum Data Rate:
The four bit value indicates the Maximum supported Data rate to the UCIe Module Partner.
The UCIe Module Partner must compare this value with its supported maximum data rate and must respond with the maximum common data rate encoding in {MBINIT.PARAM configuration resp}.
3.Clock Mode:
Clock Mode bit tells the UCIe Module Partner whether a strobe clock or a continuous clock is requested.
The Module Partner must configure its clock transmitter to match this requested mode.
The MBINIT.PARAM configuration response must reflect the same value (continuous mode uses a free-running clock).
MBINIT.PARAM (Contd..)

## Slide 18
3.Clock Phase:
The one bit value indicates the UCIe Module’s request to UCIe Module Partner for the Clock Phase support on UCIe Module’s forwarded clock.
This should only be set 1b if the maximum data rate advertised is permitted to do so.
The corresponding bit in {MBINIT.PARAM configuration resp} must be set to 1b if this was requested and the operational data rate allows it.
4.Module ID:
The UCIe Module sends its “Module ID”.
This can be used by the UCIe Module Partner if in a multi-module configuration for Byte mapping, Module enable/disable information etc.
The corresponding bits in {MBINIT.PARAM configuration resp} are reserved.
MBINIT.PARAM (Contd..)

## Slide 19
UCIe-A x32:
This bit is set to 1b when APMW bit in DVSEC UCIe Link Capability register is set to 1b (OR) ‘Force x32 width mode in x64 Module’ in the PHY Control register is set
otherwise, the bit is set to 0b.
If a x64 Advanced Package module supports width reduction to interoperate with a x32 Advanced Package Module, it uses this information from its link partner to condition the results during MBINIT.REVERSALMB.
The corresponding bits in {MBINIT.PARAM configuration resp} are reserved
MBINIT.PARAM (Contd..)

## Slide 20
MBINIT.PARAM (Contd..)

## Slide 21: MBINIT.PARAM (Contd..)
DIE 0 : UCIe Module
DIE 1 : UCIe Module Partner
{MBINIT.PARAM configuration req}
{MBINIT.PARAM configuration resp}
.
MBINIT.CAL

## Slide 22
This state is used to perform any calibration needed
Tx Duty Cycle correction
Receiver offset
Vref calibration.
This state is common for both Advanced Package and Standard Package
The UCIe Module maintains tri-state on all its mainband Transmitters, and mainband Receivers are permitted to be disabled in this state.
MBINIT.CAL

## Slide 23: MBINIT.CAL (Contd..)
DIE 0 : UCIe Module
DIE 1 : UCIe Module Partner
{MBINIT.CAL Done req}
{MBINIT.CAL Done resp}
MBINIT.REPAIR CLK

## Slide 24
This sub-state is used to detect and apply repair to clock and track Lanes for Advanced Package and for functional check of clock and track Lanes for Standard Package.
Signal Group | Full Form / Description
TCKP_P / RCKP_P | Transmit / Receive Clock Positive (P-side)
TCKN_P / RCKN_P | Transmit / Receive Clock Negative (P-side)
TTRK_P / RTRK_P | Transmit / Receive TRacKing Signal
TRDCK_P / RRDCK_P | Transmit / Receive ReDundant ClocK
MBINIT.REPAIRCLK

## Slide 25: MBINIT.REPAIRCLK for Std Package
DIE 0 : UCIe Module
DIE 1 : UCIe Module Partner
When ready to receive pattern on RCKP_L,RCKN_L and RTRK_L
{ MBINIT.REPAIRCLK init Req }
{ MBINIT.REPAIRCLK init Resp }
--------------------------------------
Sends 128 iterations of clock repair patterns(16 clock cycles followed by 8 cycles of low) on TCKP_L,TCKN_L and TTRK_L
Detects this pattern on RCKP_L,RCKN_L and RTRK_L. Detection is considered successful if at least 16 consecutive cycles of clock repair pattern are detected.it logs the detection result for RCKP_L,RCKN_L and RTRK_L.
MBINIT.REPAIRCLK done resp}
{ MBINIT.REPAIRCLK result Resp }
{ MBINIT.REPAIRCLK result Req }
If detection is not success on any one of the RCKP_L,RCKN_L and RTRK_L
Both goes to TRAINERROR after TRAINERROR handshake
If detection is successful
MBINIT.REPAIRCLK done Req
MBINIT.REPAIRVAL

## Slide 26: MBINIT.REPAIRCLK for Advanced Package
DIE 0 : UCIe Module
DIE 1 : UCIe Module Partner
ready to receive pattern on RCKP_L, RCKN_L, RTRK_L, and RRDCK_L
{ MBINIT.REPAIRCLK init Req }
{ MBINIT.REPAIRCLK init Resp }
--------------------------------------
Sends 128 iterations of clock repair patterns(16 clock cycles high followed by 8 cycles of low) on TCKP_L only
Detects this pattern on RCKP_L,RCKN_L and RTRK_L & RRDCK_L.Detection is considered successful if atleast 16 consecutive cycles of clock repair pattern are detected.it logs the detection result for RCKP_L,RCKN_L and RTRK_L &RRDCK_L
{ MBINIT.REPAIRCLK result Resp }
{ MBINIT.REPAIRCLK result Req }
Detection successful only on RCKP_L
No repair
Detected on any of them unsuccessfully
Detected on any 2
Electrical short
Repair is needed
Above steps are repeating for TCKN_L,TTRK_L and TRDCK_L

## Slide 27: MBINIT.REPAIRCLK for Advanced Package (Contd..)
DIE 0 : UCIe Module
DIE 1 : UCIe Module Partner
If a repair is needed for one of the clock or track pins (CKP,CKN or TRK) and a repair resource is available ,repair is applied by Module Partner
{MBINIT.REPAIRCLK apply repair Req }
{MBINIT.REPAIRCLK apply repair Resp }
Sends 128 iterations of clock repair patterns(16 clock cycles high followed by 8 cycles of low) on TCKP_L only
{ MBINIT.REPAIRCLK check repair init Resp }
{ MBINIT.REPAIRCLK check repair init Req }
Above steps are repeating for TCKN_L,TTRK_L and TRDCK_L
If repair is applied,UCIe module check the repair success by applying clock repair pattern and checking on the receiver
MBINIT.REPAIRCLK check results req
MBINIT.REPAIRCLK check results resp
Repair not successful
Both go to TRAINERROR
Repair is successful detected only on RCKP_L
MBINIT.REPAIRCLK done resp
MBINIT.REPAIRCLK done req
-------------------------------------------
--------------------------------------------
--------------------------------------------
REPAIRVAL
ready to receive and check clock repair pattern.

## Slide 28: UCIe Link Training
V.SRAVANTHI
CHIPWEAVE TECHNOLOGIES PVT LTD

## Slide 29: CONTENTS
Introduction
Link Training Basic Operations
Transmitter initiated Data to Clock Point Test
Transmitter initiated Data to Clock Eye Width Sweep

## Slide 30
UCIe link training is the process of detecting, aligning, calibrating, and validating a die-to-die link before enabling high-speed data transfer.
Link Training Basic Operations will be used in main band initialization, training and margining
UCIe Link Training

## Slide 31
In this mode, the Transmitter initiates the data to clock training on all Lanes in the module at a single PI phase.
When not performing the actions relevant to this state:
Transmitter initiated Data to Clock Point Test
Signal / Component | State / Behavior
Data, Valid, and Track Transmitters | Drive LOW
Clock Transmitters | Held differential LOW (for differential clocking) or simultaneous LOW (for quadrature clocking)
Data, Valid, and Clock Receivers | Enabled
Track Receiver | Permitted to be disabled
Phase Interpolator

## Slide 32
Parameter | Sideband Message Field | Options
Clock sampling / PI phase control | Clock Phase control at Transmitter | Eye Center found by training
 |  | Eye Left Edge found by training
 |  | Eye Right Edge found by training
Tx Pattern Generator Setup | Data Pattern (for Data Lanes) | LFSR Pattern for Data Lanes
 |  | Per-Lane ID pattern for Data Lanes
 | Valid Pattern (for Valid Lanes) | VALTRAIN pattern for Valid Lanes
Tx Pattern Mode Setup | Pattern Mode | Burst Mode: Uses Burst Count / Idle Count / Iteration Count
 |  | Continuous Mode: Less Burst count to indicate number of UI of transmission, Idle Count = 0, Iteration Count = 1
Rx Compare Setup | Maximum Comparison error threshold | Maximum comparison error threshold
 | Comparison Mode | Per-Lane or aggregate error compare
Transmitter initiated Data to Clock Point Test

## Slide 33: Transmitter initiated Data to Clock Point Test(Contd..)
DIE 0 : UCIe Module
DIE 1 : UCIe Module Partner
Once the data to clock training parameters for its Receiver are setup
{Start Tx Init D to C point test req}
{Start Tx Init D to C point test resp}
The UCIe Module resets the LFSR (scrambler) on its main band Transmitters
{LFSR clear error resp}
{LFSR clear error req}
performs the comparison on its Receivers for each UI during the pattern transmission based on “Rx Compare Setup” and logs the results
The UCIe Module sets up the Transmitter parameters
{Tx Init D to C results req}
{Tx Init D to C results resp}
sends the pattern selected through
“Tx Pattern Generator Setup”
The UCIe Module stops sending the pattern on its Transmitters
{End Tx Init D to C point test resp}
{End Tx Init D to C point test req}
-------------------------------------------
-------------------------------------------
-------------------------------------------
The UCIe Module Partner resets the LFSR and clears any prior compare results on its main band Receivers
Completed

## Slide 34
Signal / Component | Description
Mode Operation | The Transmitter initiates the data-to-clock training on all lanes in the module and sweeps through the sampling PI phases.
Purpose | Used for data-to-clock alignment training and for checking system margin.
Data, Valid, and Track Transmitters | Driven LOW when actions relevant to this state are not being performed.
Clock Transmitters | Held differential LOW (for differential clocking) or simultaneous LOW (for quadrature clocking).
Data, Valid, and Clock Receivers | Remain enabled during this mode.
Track Receiver | Permitted to be disabled.
Transmitter initiated Data to Clock Eye Width Sweep

## Slide 35: Transmitter initiated Data to Clock Eye Width Sweep (Contd..)
DIE 0 : UCIe Module
DIE 1 : UCIe Module Partner
Once the data to clock training parameters for its Receiver are setup
{Start Tx Init D to C eye sweep req}
{Start Tx Init D to C eye sweep resp}
The UCIe Module resets the LFSR (scrambler) on its main band Transmitters
{LFSR clear error resp}
{LFSR clear error req}
performs the comparison on its Receivers for each UI during the pattern transmission based on “Rx Compare Setup” and logs the results
The UCIe Module sets up the Transmitter parameters
{Tx Init D to C results req}
{Tx Init D to C results resp}
sends the pattern selected through “Tx Pattern Generator Setup”
The UCIe Module stops sending the pattern on its Transmitters
{End Tx Init D to C eye sweep resp}
{End Tx Init D to C eye sweep req}
-------------------------------------------
-------------------------------------------
-------------------------------------------
The UCIe Module Partner resets the LFSR and clears any prior compare results on its main band Receivers
Completed

## Slide 37
revision