## Slide 1: Control & Datapath in SoC IFC
V.SRAVANTHI
DESIGN ENGINEER
CHIPWEAVE TECHNOLOGIES PVT LTD

## Slide 2: CONTENTS
Control Path in SoC IFC
Datapath in SoC IFC

## Slide 3
Clock & Reset Control
clk
clk_cg
soc_ifc_clk_cg
rdc_clk_cg
cptra_pwrgood
cptra_rst_b
Boot FSM Control
ready_for_fuses
boot_fsm_ps cptra_noncore_rst_b cptra_uc_rst_b
iccm_unlock
AXI4 Slave Interface Control
soc_req_dv soc_req_hold soc_req_error
AHB-Lite Slave Interface Control
uc_req_dv
uc_req_hold uc_req_error
Debug Control
BootFSM_BrkPoint_valid BootFSM_BrkPoint_Latched cptra_ss_debug_intent cptra_uncore_dmi_locked_reg_en cptra_uncore_dmi_unlocked_reg_en
Fuse & Lock Control
fuse_done
fuse_wr_done_reg_write_observed
CPTRA_FUSE_WR_DONE
CPTRA_CAP_LOCK
CPTRA_OWNER_PK_HASH_LOCK
stable_owner_key_en
ss_ocp_lock_in_progress
Security Control
valid_mbox_users
valid_trng_user
valid_fuse_user
valid_sha_user
security_state.debug_locked
scan_mode
Arbitration Control
mbox_req_dv
mbox_req_hold
sha_req_dv
sha_req_hold
dma_reg_req_dv
dma_reg_req_hold
soc_ifc_reg_req_dv
soc_ifc_reg_req_hold
Interrupt Control Signals
soc_ifc_error_intr
soc_ifc_notif_intr
timer_intr
nmi_intr
t1_timeout_p
t2_timeout_p
Control Path in SoC IFC

## Slide 4: SOC_IFC Request and Data Routing Path
SoC Host
(AXI)
Cwtrust uC
(AHB Lite)
AXI_SUB
AHB_SLV_IFC
SOC_IFC_ARB Address Decoder / Mux
Mailbox
SHA
Dynamic Memory Access(DMA)
Debug Module Interface (DMI)
SOC_IFC_REG
Functional Regs Fuse Regs Security Status
Mailbox SRAM
SHA SRAM
DMA Engine
dmi_reg_wdata
dmi_reg_rdata
soc_ifc_reg_ req_data
mbox_req_data
mbox_rdata
sha_req_data
sha_rdata
dma_req_data
dma_rdata
AXI Addr /
Data/
User/ID
HADDR/
HWDATA
soc_req.addr /soc_req.wdata/
soc_req.wstrb /soc_req.user /
soc_req.id
uc_req.addr
uc_req.wdata
m_axi_w_if m_axi_r_if

## Slide 5: Read Return Datapath
SOC_IFC_REG
soc_ifc_ reg_rdata
MAILBOX mbox_rdata
mbox_dir_rdata
SHA ENGINE sha_rdata
DMA ENGINE dma_reg_rdata
DMI / DEBUG cwtrust_uncore_ dmi_reg_rdata
SOC_IFC_ARB
Read Data MUX
soc_req_rdata (AXI Read)
uc_req_rdata
(AHB Read)
SoC Host
Cwtrust uC
AXI_SUB
AHB_SLV_IFC